###### APPENDIX D

AASHTO REPORT EXAMPLE

PROJECT 040 CN 239 H 6570 01C

-40-D-(   )A

I-40; DENNISON – COUNTY LINE

FLAGSTAFF – HOLBROOK HIGHWAY

INTERSTATE 40

AASHTO CONTROLLING DESIGN CRITERIA REPORT

SEPTEMBER 2005

PREPARED FOR:

ARIZONA DEPARTMENT OF TRANSPORTATION

INTERMODEL TRANSPORTATION DIVISION

ROADWAY ENGINEERING GROUP

ROADWAY PREDESIGN

PREPARED BY:

AZTEC ENGINEERING

4561 E. MCDOWELL ROAD

PHOENIX, AZ 85008

TABLE OF CONTENTS

PAGE

List of Existing Features Requiring Design Exceptions			ii

EB & WB I-40							ii

LUEPP ROAD TI

Crossroad								ii

Ramp A								iii

Ramp B								iii

Ramp C								iii

Ramp D								iii

Summary of AASHTO Controlling Design Criteria				1-14

Attachment #1, Vertical Curve Inventory EB					15	Attachment #1, Vertical Curve Inventory WB				16	Attachment #2, Horizontal Curve Inventory EB				17	Attachment #2, Horizontal Curve Inventory WB				18

Bridge Evaluation Request							19

### LIST OF EXISTING FEATURES REQUIRING DESIGN EXCEPTIONS

The following is a list of the existing design features requiring design exceptions based upon A Policy on Geometric Design of Highways and Streets 2004 and A Policy on Design Standards – Interstate System 2005.

#### I-40 EB

The superelevation rate is less than the recommended minimum for a posted speed of 75 mph as follows:

- Beginning MP 239.96 (HPI Sta 2312+09.72)

e existing = 0.015 ft/ft	(0.050 ft/ft less than the recommended of 0.065 ft/ft)

e minimum Method 2 = 0.025 ft/ft		Method 2 Speed = 73 mph

The bridge structural capacity is less than the recommended HS 20 loading as follows:

- MP 248.99 EB Tucker Flat Bridge #336 – HS 11.11

## I-40 WB

The existing shoulder width is less than the recommended 4 ft (inside) shoulder as follows:

- MP 250.25 to MP 239.96 – 1 ft less than recommended.

The superelevation rate is less than the recommended minimum for a posted speed of 75 mph as follows:

- Beginning MP 241.38 (HPI Sta 2312+21.69)

e existing = 0.015 ft/ft	(0.050 ft/ft less than the recommended of 0.065 ft/ft)

e minimum Method 2 = 0.025 ft/ft		Method 2 Speed = 73 mph

The vertical curve stopping sight distance is less than the recommended as follows:

- Beginning MP 246.99 (VPI Sta 2682+00.00) – Existing Speed = 75 mph
3 ft less than the recommended 843 ft.

LEUPP ROAD T.I.

## Crossroad

The superelevation rate is less than the recommended minimum for a posted speed of 30 mph as follows:

- Beginning MP 245.39 (HPI Sta 3+99.21)

e existing = 0.015 ft/ft	(0.027 ft/ft less than the recommended of 0.042 ft/ft)

e minimum Method 2 = -0.137ft/ft		Method 2 Speed = 48 mph

The geometry and/or structural criteria of the bridge barrier does not meet AASHTO recommendations as follows:

- MP 245.39 Leupp TI UP (#1317) – bridge barrier

## RAMP A

The existing degree of curve exceeds the recommended maximum of 5o 58’ as follows:

- HPI Sta 10+41.78 – 4o 2’ greater than the maximum.

- HPI Sta 3+12.34 – 0o 2’ greater than the maximum.

## RAMP B

The existing degree of curve exceeds the recommended maximum of 5o 58’ as follows:

- HPI Sta 4+50.00 – 0o 2’ greater than the maximum.

- HPI Sta 12+54.03 – 4o 2’ greater than the maximum.

## RAMP C

The vertical curve stopping sight distance is less than the recommended as follows:

- VPI Sta 10+00.00 - Existing Speed = 44 mph

164 ft less than the recommended 529 ft.

## RAMP D

The superelevation rate is less than the recommended minimum for “(see Note #1 below)” as follows:

- HPI Sta 6+77.20

e existing = 0.015 ft/ft	(0.030 ft/ft less than the recommended of 0.045 ft/ft)

e minimum Method 2 = -0.059 ft/ft		Method 2 Speed 70 mph

The vertical curve stopping sight distance is less than the recommended as follows:

- VPI Sta 1+00.00 - Existing Speed = 41 mph

203 ft less than the recommended 543 ft.

- VPI Sta 6+00.00 - Existing Speed = 47 mph

120 ft less than the recommended 543 ft.

Note # 1

- If the ramp is signed with a posted speed, use “a posted speed of 50 mph.”

- If the ramp does not have a signed posted speed, use “an assumed design speed of XX mph.”

- See 2009 AASHTO Guide: Traffic Interchange Criteria; Ramps; Design Speed discussions.